## Slide 1: StandUp
ENGINEERING DESIGN & MODELLING
An adjustable, foldable laptop stand — from user need to tested prototype
[Your name] · [Course code] · [Date]
SIDE VIEW · θ = 15°–40°
Notes: Introduce yourself and the project. One-sentence pitch: 'StandUp is a foldable laptop stand that raises the screen to eye level, designed and verified using the engineering design process and mechanics-based modelling.' Replace the placeholder name/course/date. NOTE: this deck uses a worked example prototype — swap in your own prototype's name, drawing and numbers wherever you see them.

## Slide 2: The problem: laptops bend our necks
Chart: Load on the neck vs. forward head tilt (lb)
| 0° | 15° | 30° | 45° | 60°
Effective load on neck (lb) | 12 | 27 | 40 | 49 | 60
Source: Hansraj, K.K. (2014), Surgical Technology International 25, 277–279
5×
more load on the neck at 60° tilt than when upright (12 → 60 lb)
DESIGN NEED
Raise the screen to eye level while keeping the keyboard at a comfortable typing height — and make it light enough to carry every day.
Notes: Motivate the project with data, not opinion. Hansraj (2014) modelled the effective load on the cervical spine as the head tilts forward: roughly 12 lb upright rising to 60 lb at 60 degrees. A laptop on a desk forces ~30-45 degrees of neck flexion. That is the problem we translate into an engineering need. (Replace with the need your own prototype addresses.)

## Slide 3: Following the engineering design process
1
Empathise
Observed how people use laptops; listed pain points
2
Define
Wrote a problem statement and measurable specs
3
Ideate
Sketched 3 concepts and scored them
4
Prototype
Modelled in CAD, analysed, and built
5
Test
Verified the prototype against every spec
Iteration is the point. Test results fed back into the specs and the CAD model — two design versions were built (see Iteration).
Notes: Walk through the five stages briefly (about 20 seconds each). The point to land: this was not 'build then hope' — each stage produced an artefact (observations, spec table, concept matrix, CAD + calculations, test plan). The dashed banner shows the loop: testing changed the design. Highlighted stages 4 and 5 are where the engineering modelling lives.

## Slide 4: From user needs to measurable specs
Customer need (voice of user) | Engineering metric | Target
Screen at eye level | Tilt angle range | 15° – 40°
Doesn't bounce while typing | Tray deflection under 5 kg | ≤ 1.5 mm
Won't break or collapse | Factor of safety on yield | ≥ 3
Fits in a backpack | Folded thickness | ≤ 20 mm
Easy to carry daily | Total mass | ≤ 0.8 kg
Affordable for students | Material cost | ≤ $12
Translating vague wishes into numbers is what makes a design testable: every target above is later verified by a calculation, a CAD check, or a physical test.
Notes: This is a simplified House-of-Quality step: customer needs on the left, the engineering metric that captures each need in the middle, and a target value on the right. Explain WHY each target was chosen: e.g. 1.5 mm deflection is below what a typist can feel; 20 mm folded thickness fits a laptop sleeve pocket; factor of safety >= 3 is typical for consumer products with uncertain loading. Replace with your own spec table.

## Slide 5: Choosing a concept with a decision matrix
A
Fixed wedge
Solid block; very stable, not adjustable or portable
B
Scissor lift
Height-adjustable; many parts, wobbly, costly
C
Hinged tray + adjustable leg
Folds flat; 3 leg positions; few parts
Criterion | Weight | A | B | C
Stability | 25% | 5 | 3 | 4
Portability | 20% | 2 | 4 | 5
Adjustability | 20% | 1 | 5 | 4
Cost | 15% | 5 | 2 | 4
Manufacturability | 10% | 5 | 2 | 4
Aesthetics | 10% | 3 | 4 | 4
Weighted score (out of 5) | 100% | 3.40 | 3.45 | 4.20
Scores 1 (poor) – 5 (excellent). Weights reflect the user needs on the previous slide.
Notes: Explain the method: weights sum to 100% and come from the needs (portability and adjustability matter most to our users). Each concept is scored 1-5 per criterion; the weighted sum picks the winner. Concept C wins with 4.20 vs 3.40 (A) and 3.45 (B). Mention sensitivity: if you changed weights by +/-10%, C still wins — a good robustness point. Replace with your own concepts/scores.

## Slide 6: The final design: four functional parts
1
2
3
4
θ
Side view, not to scale
1
Tray (2 mm Al 6061)
Carries the laptop; sized for stiffness, not just strength
2
Adjustable rear leg
Three notches set the tilt from 15° to 40°
3
Hinge joints
Let the stand fold flat to about 12 mm
4
Front lip
Stops the laptop sliding; rounded to protect users
Notes: Replace the schematic with a screenshot of your own CAD model (an isometric view plus a labelled exploded view works well). Each part should have a clear function, and you should be able to say why you chose its material and geometry. Point out that the dashed leg in the drawing shows the adjustable positions.

## Slide 7: Modelling the tray as a beam
F = 49 N (5 kg design load)
L = 250 mm
M = F·L / 4 σ = M·c / I I = b·t³ / 12
δ = F·L³ / (48·E·I) FoS = σy / σ
ASSUMPTIONS
Material: Al 6061-T6 — E = 68.9 GPa, σy = 276 MPa
Tray: b = 250 mm wide, t = 2 mm thick
Static load, linear-elastic, small deflection
18.4 MPa
Peak bending stress σ
15
Factor of safety (target ≥ 3)
1.39 mm
Mid-span deflection δ (limit 1.5 mm)
Notes: Show the model: idealise the tray as a simply supported beam with a centre point load — the worst case, because a real laptop spreads its weight. Walk through M = FL/4 = 3.07 N·m, I = b t^3/12 = 1.67e-10 m^4, sigma = Mc/I = 18.4 MPa, and delta = FL^3/(48EI) = 1.39 mm. State the assumptions out loud — examiners love hearing what the model ignores (dynamic loads, fatigue, stress concentrations at holes and bends).

## Slide 8: Stiffness, not strength, sets the thickness
Chart: Mid-span deflection vs. tray thickness
| 1 mm | 1.5 mm | 2 mm | 2.5 mm | 3 mm | 4 mm
Predicted deflection (mm) | 11.12 | 3.3 | 1.39 | 0.71 | 0.41 | 0.17
Deflection limit (1.5 mm) | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5
Strength is easy
At 2 mm the stress is only 18 MPa — factor of safety 15.
Stiffness is the limit
Deflection scales as 1/t³: 2 mm gives 1.4 mm, just under the 1.5 mm limit.
Mass scales linearly
Thicker is 8× stiffer per doubling, but only 2× heavier — so we stop at the limit.
Notes: This is the 'I understand the subject' slide. Most students check stress only. Here the design is stiffness-driven: because deflection goes as 1/t^3 while stress goes as 1/t^2, the deflection limit binds first. Sweep thickness in the model (or in a CAD parametric study) and pick the thinnest tray that meets the limit — this minimises mass and cost. Values: 1 mm -> 11.12 mm; 1.5 mm -> 3.3 mm; 2 mm -> 1.39 mm; 2.5 mm -> 0.71 mm; 3 mm -> 0.41 mm; 4 mm -> 0.17 mm.

## Slide 9: Parametric CAD and FEA validation
1
Sketch
Fully constrained profile with driven dimensions
2
Parametrise
Tie thickness, span and tilt to named parameters
3
Simulate
Mesh, fix supports, apply 49 N load
4
Correlate
Compare FEA with hand calc; target within 10%
Insert your CAD render or FEA stress plot here
Colour map of von Mises stress or displacement works best
WHY VALIDATE?
Two independent methods agreeing builds trust in the model
Mesh convergence: refine until results change < 2%
Parameters let one model explore many design variants
Notes: Replace the dashed box with a real screenshot from your CAD/FEA package (SolidWorks, Fusion 360, Onshape, Ansys...). Explain the four-step workflow, and especially the correlation step: hand calculation and FEA should agree closely for a simple geometry; if they don't, either the mesh, the boundary conditions or the idealisation is wrong. Mention mesh convergence if you ran it.

## Slide 10: Building it: materials, process and cost
Part | Material | Process | Cost
Tray + base plate | Al 6061-T6, 2 mm sheet | Laser cut + bend | $4.50
Adjustable rear legs (2) | Al tube Ø12 × 1 mm | Cut + drill | $2.80
Hinge pins & bolts | Stainless steel | Off the shelf | $1.20
Fasteners & washers | Zinc-plated steel | Off the shelf | $0.90
Anti-slip feet (4) | Silicone rubber | Press fit | $1.00
Total (target ≤ $12) |  |  | $10.40
Unit costs are estimates for a one-off prototype.
DESIGN FOR MANUFACTURE
Standard stock
Sheet and tube sizes off the shelf
Few unique parts
Only 6 parts, no welding or glue
Forgiving tolerances
Slotted holes absorb ±0.5 mm error
Notes: Cover materials, manufacturing process and cost. Total BOM is $10.40 against a $12 target. Link choices back to the specs: aluminium is light and corrosion-resistant; laser cutting plus bending needs no tooling; slotted holes make assembly tolerant of fabrication error. Replace with your actual parts list, photos of the build, and real costs.

## Slide 11: Verification plan: model vs. measurement
Test | Method | Pass criterion | Model predicts | Measured
Deflection | Dial gauge, 5 kg at centre | ≤ 1.5 mm | 1.39 mm | [ fill in ]
Strength | 10 kg for 10 min, check for set | No permanent set | FoS 15 at 5 kg | [ fill in ]
Tilt range | Protractor at each leg notch | 15° – 40° | 15°, 28°, 40° | [ fill in ]
Folded thickness | Callipers | ≤ 20 mm | ≈ 12 mm | [ fill in ]
Mass | Kitchen scale | ≤ 0.8 kg | ≈ 0.5 kg | [ fill in ]
Goal: measured values within about 10% of the model. Larger gaps tell us which assumption in the model to revisit.
Notes: Every spec from slide 4 gets a test with a pass criterion. The 'Model predicts' column comes from the calculations; the 'Measured' column is blank for you to fill in after testing. Report honestly: if a measurement misses the target or disagrees with the model, explain why (e.g. bolt clearance adds play, the point-load idealisation, sheet thickness tolerance). That reflection scores higher than a perfect table.

## Slide 12: Iteration: what version 2 fixed
VERSION 1 · 1 mm tray
11.1 mm
predicted deflection — a springy, bouncy keyboard
VERSION 2 · 2 mm tray
1.4 mm
predicted deflection — 8× stiffer for only 2× the sheet mass
Problem | Tray flexed when typing | Rear legs slid on the desk | Hinge wobbled sideways
Change | Doubled thickness to 2 mm | Added silicone feet and serrated notches | Swapped rivets for shoulder bolts
Result | Meets the deflection limit | Holds position on smooth desks | Rigid, repeatable pivot
Notes: Show that testing changed the design. The 1 mm to 2 mm change is directly traceable to the model: delta goes as 1/t^3, so doubling thickness cuts predicted deflection by 8x (11.1 mm to 1.4 mm). The other two fixes are practical observations from handling the prototype. Replace with the real issues you found and fixed.

## Slide 13: Beyond the calculations
Safety
Rounded edges and corners, pinch-free hinge gap, factor of safety above 3 on the test load.
Sustainability
One recyclable material family, no adhesives, every part repairable or replaceable.
Ergonomics
Tilt range lets screen top sit near eye level for different desk and user heights.
Limitations
Static loads only. Fatigue, vibration and bend-radius stress concentrations were not modelled.
Notes: Show engineering maturity: a design is more than its stress number. Safety, sustainability and ergonomics are standard design considerations; the limitations card is where you state what your model does NOT capture. Being upfront about limitations is a strength, not a weakness.

## Slide 14
Conclusion and next steps
01
Need to spec
A posture problem became six measurable targets.
02
Model-led design
Beam theory showed stiffness, not strength, sets the thickness (1.4 mm vs 1.5 mm limit).
03
Built and iterated
Version 2 meets the spec at about $10 and 0.5 kg.
NEXT STEPS
Fatigue and vibration analysis of hinge and leg joints
Topology-optimised tray cut-outs to reduce mass further
User trial with 10 participants to validate comfort
Thank you
Questions?
Notes: Close by restating the three messages: need to spec, model-led design, build and iterate. Then the next steps (these show you know what a fuller study would include). Invite questions.